Goblet Mesh	Christopher McKinney
A goblet of this form can be defined as a 14-tuple langle w_g`r_o`h_uc`r_c`h_lc`r_s`h_s`R_bd`h_bd`r_bl`h_bl`R_bs`r_bs`h_bs rangle (refer to the above diagram for the associated measures). Note that for the purpose of hs, the top of the stem is defined as the bottom of the spheroid that defines the exterior of the lower cup, even though the bottom of that spheroid is excluded from the point set. However, for all other purposes, the “stem” extends all the way up to where it meets the lower cup (the intersection on the outer edge). The set of points P defining the edge of the central cross-section of the material (as displayed in the diagram above) can be defined as follows:
{}"Let"~%DELTA_uc=r_c-r_o,`R_c=r_c+w_g,`H_lc=h_c+w_g,`y_c=h_bs+h_bs+h_bl+h_bd+h_s+H_lc, newline r_L=w_g over 2 ,`x_L=r_o+r_L,`y_L=y_c+h_uc,`%DELTA_s=r_bl-r_s,`v_s=h_s over 2 ,`ys=h_bs+h_bl+h_bd+v_s, newline %DELTA_bd=R_bd-r_bl,`v_bd=h_bd over 2 ,`y_bd=h_bs+h_bl+v_bd,`%DELTA_bl=r_bs-r_bl,%DELTA_bs=R_bs-r_bs, newline {}"and"`v_bs=h_bs over 2 .
{}"Let"~%OMEGA_s="min"a`"and"`%theta_lc="min"b newline {}"where" R_c cos b - %DELTA_s a^2 - r_s=0,`H_lc sin b +y_c - v_s a - y_s=0, newline a>=1,`"and"`-%pi over 2<=b<=0 .
{}"Let"~bold L=lbrace (r_L cos a+x_L,`r_L sin a+y_L)`"|"`0<=a<=%pi rbrace, newline bold a=lbrace (%DELTA_uc a^2+r_c,`h_uc a+y_c)`"|"`0<=a<=1 rbrace,`bold A=lbrace (%DELTA_uc a^2+R_c,`h_uc a+y_c)`"|"`0<=a<=1 rbrace, newline bold b=lbrace (r_c cos a,`h_lc sin a+y_c)`"|"`-%pi<=a<=0 rbrace,`bold B=lbrace (R_c cos a,`H_lc sin a+y_c)`"|"`%theta_lc<=a<=0 rbrace, newline bold C=lbrace (%DELTA_s a^2+r_s,`v_S a+y_s)`"|"`-1<=a<=%OMEGA_s rbrace,`bold D=lbrace (-%DELTA_bd sin a+r_bl,`v_bd cos a+y_bd)`"|"`-%pi<=a<=0 rbrace, newline bold E=lbrace (-%DELTA_bl cos a+r_bs,`h_bl(sin a+1)+h_bs)`"|"`-pi/2<=a<=0 rbrace, newline bold F=lbrace (%DELTA_bs sin a+r_bs,`v_bs(cos a+1))`"|"`-pi<=a<=0 rbrace,`"and"`bold G=lbrace (r_bs a,`0)`"|"`-1<=a<=1 rbrace .
{}"Let"~"mirror"bold S:=bold S union lbrace (-x,y)`"|"`(x,y) in bold S rbrace .
bold P="mirror" bold B union "mirror" bold A union "mirror" bold L union "mirror" bold a union bold b union "mirror" bold C union "mirror" bold D union "mirror" bold E union "mirror" bold F union bold G
The form of the goblet is obtained by rotating the shell defined by P about the y-axis:

The goblet can hold liquid (not touching the lip) of volume Vhold, which can be calculated using the integration formula for the volume of the inner wall of the cup:
V_hold=int from 0 to h_uc %pi(%DELTA_uc y^2 over h_uc^2+r_c)^2 dy +int from 0 to h_lc %pi r_c^2(1-y^2 over h_lc^2) dy
The volume of glass Vglass required to form the goblet can be calculated using the integration formula for the volume of all of the components of the goblet (except for the lip, for which we can use the formula for the volume of a torus):
{}"Let"~V_L=%pi^2 x_L r_L^2 ,`V_uc=int from 0 to h_uc %pi(%DELTA_uc y^2 over h_uc^2+R_c)^2 dy - int from 0 to h_uc %pi(%DELTA_uc y^2 over h_uc^2+r_c)^2 dy, newline U=H_lc-v_s(%OMEGA_s-1),`V_lc=int from 0 to U %pi R_c^2(1-y^2 over H_lc^2) dy-int from 0 to {"min"lbrace U,h_lc rbrace} %pi r_c^2(1-y^2 over h_lc^2) dy, newline V_s=int from -v_s to {%OMEGA_s v_s} %pi(%DELTA_s y^2 over v_s^2+r_s)^2 dy,` V_bd=int from -v_bd to v_bd %pi(%DELTA_bd sin(acos(y over v_bd))+r_bl)^2 dy, newline V_bl=int from 0 to h_bl %pi(%DELTA_bl cos(asin(y over h_bl))+r_bs)^2 dy,` V_bs=int from -v_bs to v_bs %pi(%DELTA_bs sin(acos(y over v_bs))+r_bs)^2 dy
V_glass=V_L+V_uc+V_lc+V_s+V_bd+V_bl+V_bs
The goblet that has been shown in the diagrams has been the goblet defined by the tuple langle 0.2`2.3`6.6`3.3`3.3`0.25`2`0.7`0.4`0.5`2`2.4`2.3`0.2 rangle . This goblet has a holding volume of approximately 259.60 cm3 and a total glass volume of 132.72 cm3. 3r_bs=6.9"cm," and the center of mass is known to be in the “bottom” section of the goblet since the glass has (presumably) uniform density and V_bottom=V_s+V_bd+V_bl+V_bs approx 92.535"cm"^3`>`V_cup=V_L+V_uc+V_lc approx 40.186"cm"^3 , and since the height of the bottom section h_bottom=v_s(%OMEGA_s-1)+h_s+h_bd+h_bl+h_bs approx 4.6388"cm," the center of mass is known to be below 6.9cm. The thinnest glass is along the walls of the cup, where it has a thickness of 0.2cm (the walls terminate at the lip, which has a minor toroidal diameter of 0.2cm), at the edge of the base, which has a height (and as such a minor toroidal diameter) of 0.2cm, and at the middle of the stem, where it has a diameter of 0.5cm.